OFFER FOR LICENSED OPERATORS

CONTENT

INTRODUCTION	6

I. SWITCHED TRAFFIC ROUTING SERVICE	6

I.1. Description of Points of Interconnection	6

I.1.1. Locations and Types of Signals	6

I.2. Technical Terms	7

I.2.1. Traffic Routing Services	7

I.2.1.1. Pricing of the fixed-line portion	7

I.2.1.2. Direct interconnection offer	7

I.2.1.3. Indirect interconnection offer	7

I.2.1.4. Support for portability	7

I.3. Organisation of interconnection ports	7

I.3.1. Responsibility for sizing of links	8

I.4. Traffic Termination Tariffs	8

I.4.1. Rate for Termination of National Voice Traffic on CAMTEL’s Network	8

I.4.2. National SMS/MMS Rate	8

I.4.3 A2P SMS	8

I.4.4. Pricing of MT SMS or Bulk SMS and A2P	8

I.4.5. International Voice/SMS/MMS Rate	9

II. DESCRIPTION OF INTERFACES AND INTERCONNECTION SIGNALLING PROTOCOLS	9

II.1. ELECTRICAL INTERFACES	9

II. 2. Signalling Protocols	9

III. CO-LOCATION AND INFRASTRUCTURE SHARING	9

III.1. Co-location and Sharing Offer	9

III.1.1. Technical Terms for Co-location	9

III.1.1.1. Terminal Equipment Hosting	10

III.1.1.2. Towers	10

III.1.2. Terms of Access	10

III.1.3.  Power Supply	10

III.2. Co-location Rates	10

IV. 	MAXIMUM TIME LIMITS FOR THE COMMISSIONING OF THE INTERCONNECTION	11

V. SCHEDULING OF OPENING OF NEW POINTS OF INTERCONNECTION	11

VI. Implementation of Interconnection and Access Catalogues	11

VII. Block Diagram of the Mobile Network	12

VIII. APPENDICES	13

VIII.1. PRICING OF TOWERS	13

VIII.1.1.  Introduction	13

VIII.1.2.  Pricing Parameters	13

VIII.1.3.  Analysis of Pricing Parameters	13

VIII.1.4.  Classification of Towers	14

DEFINITIONS

For the purposes of this catalogue, the following terms shall have the definitions hereunder:

- CEPT: European Conference of Postal and Telecommunications Administrations.

- Co-location: provision of space and technical resources required to host and connect, under reasonable conditions, the relevant equipment of an operator as part of a reference offer.

- Half circuit: Half circuit, or a circuit that operates with unidirectional transmission.

- Terminal equipment: Any device, installation or set of installations meant to be connected to a network termination point, and which transmits, receives or processes electronic communications signals. This does not include equipment that enables access to audiovisual communication services broadcast over the air or distributed by cable, except where such equipment also enables access to other electronic communications services.

- Full circuit: Full circuit, or a circuit that operates with bidirectional transmission.

- Beam: set of circuits that make it possible to connect two switches. It can be unidirectional or bidirectional depending on whether communications are in one or both directions.

- Certification: Expert assessment and verification exercise conducted by an approved body to certify that the prototype of electronic communications equipment and of systems complies with the regulations and technical specifications in force.

- Interconnection: Particular method of access that involves physically and logically linking the public electronic communications networks used by the same or different operators to allow users to communicate with each other or to access services provided by another operator.

- Direct Interconnection: CAMTEL routes traffic originating from a customer of the PECNO from the point of interconnection to CAMTEL’s network up to one of its subscribers.

- Indirect Interconnection: CAMTEL carries the traffic of a subscriber on its network to the point of interconnection to a PECNO’s network so that the said subscriber can use the services of the PECNO in question.

- Transit interconnection: Two PECNOs interconnect their networks using CAMTEL’s network.

- Terminal equipment interoperability: Ability of terminal equipment to work with the network and with other terminal equipment that enable access to the same service.

- Radio installation, station or equipment: Any electronic communication installation, station or equipment that uses radio frequencies for wave propagation in free space. Radio installations notably include networks that use satellite capacities.

- ISDN: Integrated Services Digital Network

- ISUP: ISDN USER Part (SS7 signalling protocol used for communication processing)

- MGW: Media Gateway: conversion equipment or service that transforms and converts multimedia streams (voice or video) between telecommunications networks using different network standards, communication protocols, coding techniques and physical connections, such that telephone calls work properly between networks that use different technologies.

- Operator: A person or legal entity operating public electronic communications service or providing an electronic communications service to the public.

- PECNO: Public Electronic Communications Network Operator.

- PION: Point of Interconnection of Operator Networks.

- Termination point: Physical point through which users access a public electronic communications network. These connection points are part of the network.

When a telecommunication network is connected to a foreign network, the points of connection to that network are considered as termination points.

When a telecommunication network is intended to transmit signals to broadcasting installations, the points of connection to these installations are considered as termination points.

- Portability: In telephony, portability refers to the possibility for a subscriber to keep their telephone number if they change operators.

- PCM distribution frame: Distribution point of pulse-code modulation circuits. Their bandwidth is 2048kbits/s.

- Public electronic communications network: A set of electronic communications networks established or used to service the needs of the public.

- Electronic communications network: Active or passive transmission systems and, where applicable, switching and routing equipment and other resources, which make it possible to transmit signals by wire, by radio, by optical means or by other electromagnetic means: including satellite networks; fixed (circuit-switched or packets, including the Internet) and mobile terrestrial networks; systems using the electrical network, provided they are used for transmitting signals; networks used for radio and television broadcasting; and cable television networks, irrespective of the type of information broadcast.

- Value-added service: Service offered to the public over public electronic communications networks using computer systems providing access to data pertaining to specific areas to consult or exchange them.

- Data transmission service: Simple data transmission service that does not include any additional processing.

- Basic telecommunications service: International, national and local telecommunications service for telephony between fixed points, facsimile, telex and telegraph.

- Electronic communications service: service consisting wholly or mainly in the provision of electronic communications.

- Telecommunications: Any transmission, emission or reception of signs and signals, text, images, sounds or intelligence of any kind, by wire, optical, radio means or any other electromagnetic system.

- USSD: Unstructured Supplementary Service Data. The communication protocol used in a mobile network to exchange data between the client and the Operator’s or Value-Added Service Provider’s server.

# INTRODUCTION

This catalogue is published by Cameroon Telecommunications (CAMTEL) for the operation of the Mobile Licence in accordance with the provisions of Law No. 2010/013 of 21 December 2010 governing electronic communications in Cameroon, as amended and supplemented by Law No. 2015/006 of 20 April 2015, Decree No. 2012/1 640/PM of 14 June 2012 Decree No. 2012/1640/PM of 14 June 2012 to lay down conditions for interconnection, access to public electronic communications networks, and infrastructure sharing, in application of Concession Agreement No. 1 of 4 March 2020 for the deployment and operation of a public mobile electronic communications network, Decision No. 44/ART/DG/DLCI/CI of 23 July 2002 to prescribe directives on the conditions for interconnection of open public telecommunications networks.

It is valid for 2022.

This catalogue presents CAMTEL’s technical offering and tariffs for Public Electronic Communications Network Operators (PECNO) to enable all users of interconnected networks to communicate freely with each other. It covers the following interconnection offers:

- traffic routing service;

- additional services and functionalities;

- Co-location and infrastructure sharing.

Each interconnection arrangement with CAMTEL shall be subject to an interconnection agreement describing the technical and financial terms and conditions of the services offered. It is understood that:

- the rates listed in this catalogue are exclusive of tax;

- the access fees for offers or services shall be those in force on the date such offers or services are made available.

- all the services covered by this catalogue are offered within the limits of the technical conditions and capacities of CAMTEL’s infrastructure;

- a discount on the rates may be granted in the case of very large orders, long-term commitments or prepayment.

# I. SWITCHED TRAFFIC ROUTING SERVICE

## I.1. Description of Points of Interconnection

## I.1.1. Locations and Types of Signals

The points of interconnection CAMTEL offers to Public Electronic Communications Network Operators are:

| Description | Sites | Type of Signal | Type of Interconnection |
| --- | --- | --- | --- |
| MGW Yaounde | CAMTEL building Yaounde, Centre | Code No. 7 ISUP SIP protocol | Traffic termination Mobile voice |
| MGW DOUALA | CAMTEL building Douala-Bepanda | Code No. 7 ISUP SIP protocol | Traffic termination Mobile voice |

## I.2. Technical Terms

#### I.2.1. Traffic Routing Services

The technical connection offer presented in this catalogue makes it possible to use voice and data from or to PECNOs under the same conditions of quality and technical availability as for all calls made on CAMTEL’s network.

All of this traffic is brought by the PECNO to a point of interconnection of operator networks (PION) and distributed over one or two beams of circuits operated on a load-sharing basis. These beams must be carried by 2Mbit/s links. Where the traffic is carried by two separate beams, the 2Mbit/s links must be separate.

#### I.2.1.1. Pricing of the fixed-line portion

The rate for the provision of E1 ports (2Mbit/s) by CAMTEL amounts to CFAF 800,000 (tax exclusive) per E1 port per year.

#### I.2.1.2. Direct interconnection offer

CAMTEL routes traffic originating from a customer of the PECNO from the point of interconnection to CAMTEL’s network up to one of its subscribers (CAMTEL subscriber) serviced by or available via its network.

#### I.2.1.3. Indirect interconnection offer

CAMTEL carries the traffic of a subscriber on its network to the point of interconnection to a PECNO’s network so that the said subscriber can use the services of the PECNO in question.

#### I.2.1.4. Support for portability

This system allows any subscriber to keep their mobile phone number or MSISDN while changing mobile operators.

Number portability shall be taken into account in the technical processes relating to interconnection as soon as this service is effectively implemented.

## I.3. Organisation of interconnection ports

The connection capacity is defined for each PION to which the operator wishes to connect. The basic unit is the 2Mbit/s link.

#### I.3.1. Responsibility for sizing of links

A PECNO interconnecting to CAMTEL’s network shall be responsible for the sizing of the interconnection links needed to deliver its traffic to CAMTEL’s network.

The opening of a link with a PECNO shall be preceded by a series of validation and compatibility tests following the provisions of the interconnection agreement and the routing of calls to emergency, security and police services.

## I.4. Traffic Termination Tariffs

#### I.4.1. Rate for Termination of National Voice Traffic on CAMTEL’s Network

| TYPE OF COMMUNICATION | Rates for Peak Hours (7 am-8:59 pm) | Rates Off-peak Hours (9 pm-6:59 am) |
| --- | --- | --- |
| Voice calls | CFAF 12, tax excluded | CFAF 10, tax excluded |

#### I.4.2. National SMS/MMS Rate

CFAF 5 (T.E.)/SMS

### I.4.3 A2P SMS

Description and Technical Terms

CAMTEL offers operators the A2P SMS service, enabling them to send bulk SMS messages across its network to one or more users.

Technical architecture

### I.4.4. Pricing of MT SMS or Bulk SMS and A2P

The rates are set according to volume.

| Number of SMS | From 1 to 4,999 | From 5,000 to 9,999 | From 10,000 to 49,999 | From 50,000 to 999,999 | From 1,000,000 to 5,999,999 | From 6,000,000 to 7,499,999 | From 7,500,000 to 9,999,999 | Over 10,000,000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MT SMS rate in CFAF (T.E.) | 8 | 7.5 | 7 | 6.5 | 5.5 | 5 | 4.5 | 3.5 |
| A2P SMS rate in CFAF (T.E.) | 6 | 5.5 | 5 | 4.5 | 3.5 | 3 | 2.5 | 2 |

For traffic destined for the mobile networks of other Operators, the interconnection charge imposed by third party operators shall be added to the above wholesale SMS rates.

For voice or SMS traffic to premium rate numbers, CAMTEL shall deduct the cost of transit for routing the traffic and shall share the rest as follows: 60% for the provider and 40% for CAMTEL.

The cost of voice transmission shall be CFAF 10 (T.E.)/minute.

The cost of SMS transmission shall be CFAF 5 (T.E.)/SMS.

#### I.4.5. International Voice/SMS/MMS Rate

CAMTEL shall negotiate with foreign Operators, on the one hand, and with PECNOs, on the other hand, the quotas to be applied for the routing of this outgoing and incoming traffic. The agreements between CAMTEL and PECNOs shall determine precisely the quotas to be applied.

# II. DESCRIPTION OF INTERFACES AND INTERCONNECTION SIGNALLING PROTOCOLS

## II.1. ELECTRICAL INTERFACES

The connecting link shall consist of a set of 2Mbit/s links. The connection interface complies with ITU-T recommendation G.703, CEPT 2Mbit/s, 120 Wsymmetrical.

Warning, signalling, fault location and intervention procedures are defined in the interconnection agreement between CAMTEL and PECNO.

## II. 2. Signalling Protocols

The signalling protocol to be used for the interconnection of PECNOs will be signalling system No. 7 ISUP (ITU-T Recommendation No. Q.761-Q.764 1992 Specifications of ISDN User Part) or the SIP, in the NITC in Yaounde and in Douala.

The opening of a link with a PECNO shall be preceded by a series of validation and compatibility tests in accordance with the regulatory provisions and the interconnection agreement.

# III. CO-LOCATION AND INFRASTRUCTURE SHARING

## III.1. Co-location and Sharing Offer

#### III.1.1. Technical Terms for Co-location

CAMTEL shall offer the Co-location service to PECNO who want to implement the interconnection link themselves. Where the equipment is located on its premises, CAMTEL shall be notified of any intervention thereupon.

To implement an interconnection link up to a point of interconnection (PION), a PECNO may use CAMTEL’s infrastructure, within the limits of the site’s available hosting capacities (land, power supply, building, tower, conduits, etc.), to install the transmission link’s support.

Where possible, the terminal equipment used for transmission may be installed in a room reserved for the PECNO and located in CAMTEL’s building or in a room built by the PECNO on CAMTEL’s site. In both cases, the PECNO shall be responsible for the operation and maintenance of their equipment. The connection of the PECNO’s equipment to the PCM distribution frame of the PION shall be implemented by a joint CAMTEL/PECNO team.

#### III.1.1.1. Terminal Equipment Hosting

In exceptional cases, terminal equipment used for transmission may be installed in a CAMTEL transmission room. The said equipment must be installed in a watertight cabinet that may also contain the secondary power supply equipment and air conditioning. CAMTEL may, under terms to be negotiated, handle the first-level operation and maintenance of the equipment housed in its rooms.

#### III.1.1.2. Towers

With regard to towers, the requesting PECNO shall provide, in particular:

- the characteristics (radio and mechanical) of the antenna;

- the installation height on the tower;

- the weight of the antenna.

The hosted equipment must comply with the latest ITU-T and ITU-R technical standards, as well as any other technical standards set by CAMTEL in the interconnection agreement, including those related to environmental compliance.

The list of towers proposed for sharing by CAMTEL is provided in the appendices.

#### III.1.2. Terms of Access

The terms under which the PECNO shall access the room where their equipment is installed shall be specified in the interconnection agreement.

#### III.1.3.  Power Supply

The infrastructure sharing agreement shall specify the terms for the PECNO by CAMTEL, the terms of access to the equipment, the terms and conditions of maintenance, the documentation, the material to be provided by the PECNO and additional services.

## III.2. Co-location Rates

| NATURE OF SERVICE | RATE in CFAF, T.E. |
| --- | --- |
| Towers | On basis of a cost estimate according to the calculation formula below. C= ai*(Rj*Mk+En). ai: coefficient pertaining to the category of the tower. Rj: radio characteristics of the antenna Mk: mechanical characteristics of the antenna En = Characteristics of the footprint on the tower |
| Land | On basis of a cost estimate according to regions, price per m2, and surface area required (surveys, surveys, miscellaneous research). Undeveloped land: Yaounde, Douala, Kribi, Limbe: CFAF 7,000/m2/yr Other towns: CFAF 5,000/m2/yr Rural areas: CFAF 3,000/m2/yr |
| Building | DOUALA, YAOUNDE, KRIBI, LIMBE: CFAF 90,000/m2/yr Other urban areas: CFAF 60,000/m2/yr Rural areas: CFAF 40,000/m2/yr |
| Back-up power supply | CFAF 500 /KWH/month + fixed premium of CFAF 2,865/KW/month |
| Air-conditioning | Based on the equipment installed and the capacity requested. |

# IV. 	MAXIMUM TIME LIMITS FOR THE COMMISSIONING OF THE INTERCONNECTION

Subject to the availability of all interface equipment, the interconnection shall be made available within 30 days of receipt of the request.

As far as Co-location is concerned, the feasibility will be communicated to ORCEOP within a maximum period of 60 days from receipt of the request for Co-location.

The PECNOs and CAMTEL shall set out, in their agreements, the terms and conditions for communicating their traffic volumes.

The time limit for activating all the numbering resources allocated by the TRB is 10 (ten) working days upon receipt of a formal request.

# V. SCHEDULING OF OPENING OF NEW POINTS OF INTERCONNECTION

To ensure the planning of the necessary interconnection resources and to guarantee adequate sizing of traffic management capacities within CAMTEL’s network, the terms for planning and scheduling the opening of new point of interconnection may be defined.

# VI. Implementation of Interconnection and Access Catalogues

The interconnection and access agreement shall comply with interconnection and access catalogues. To this end, the provisions of the catalogues, once approved, will be taken into account in all interconnection agreements signed between CAMTEL and its partners.

# VII. Block Diagram of the Mobile Network

# VIII. ANNEXES

## VIII.1. PRICING OF TOWERS

#### VIII.1.1.  Introduction

The parameters that influence pricing can be grouped into the radio characteristics of the antennas to be installed, the mechanical characteristics, and the tower footprint.

Pricing is for the rental of space for a single antenna. The total cost is gotten by multiplying by the number of antennas.

#### VIII.1.2.  Pricing Parameters

A. Radio Characteristics of Antenna

- Frequency or range of frequencies used

- Polarisation of the antenna

- Antenna azimuth and elevation

- Radiation pattern (horizontal and vertical)

- Isotropic gain

B. Mechanical Characteristics of Antenna

- Space requirement (dimensions)

- Weight

- Windward surface (front, side)

- Wind load at a speed of 150 km/h (front, side)

- Permissible wind speed (maximum)

C. Characteristics of Tower Footprint

- Height requested for an antenna

- Number of antennas

- Linear occupation of the tower

- Mounting of the antenna (on one of the 3 sides of the tower or on one of the 3 vertical supports)

- Horizontal cable tray and vertical feeders assignment

- Feeder diameter

#### VIII.1.3.  Analysis of Pricing Parameters

Given:

- Rj 	Parameter grouping together the radio characteristics of the antenna, including the use of a single frequency (R1) or a range of frequencies (R2)

R1=10/5=2

R2=20/5=4

- Mk	parameter grouping the mechanical characteristics of the antenna, in particular the weight P (kg), the maximum windward surface S (m²), the wind load at 150 km/h, C (N).

Mk=ak.P

a1=20 where S<= 0.5 m² or C<=500N

a2=30 where 0.5<S<1m² or 500<C<1000 N

a3=40 where S>=1 m² or C>=1000 N

- Parameter grouping the characteristics of the tower footprint, in particular the requested height of the tower h (m), the linear occupation of the tower l (m), the occupancy of the cable tray.

En=bn.h²

b1=6 where l <=1m

b2=8 where 1<l<2m

b3=9 where l>=2m

Thus, the monthly cost of renting space on the tower for an antenna is gotten via the general formula below:

C =ﻪi (Rj.Mk+En)

ﻪi: Coefficient pertaining to the category of the tower

ﻪ1= 5 for category A

ﻪ2= 5 for category B

ﻪ3= 5 for category C

#### VIII.1.4.  Classification of Towers

Category A: 	towers taller than or equal to 120 m;

Category B: 	towers between 51 m and 119 m tall;

Category C: 	towers shorter than or equal to 50 m.

List of towers

| Order No. | Location of site | Height (m) | Type of tower | Category of tower |  |
| --- | --- | --- | --- | --- | --- |
| 1 | Ahala, Chefferie | 40 | S | C |  |
| 2 | Emana | 40 | S | C | Type of tower: |
| 3 | Akiriba | 40 | S | C | S= Self-supporting |
| 4 | Akoeman | 40 | S | C | G= Guyed |
| 5 | Akom II ancien | 30 | S | C |  |
| 6 | Akom II nouveau | 50 | S | C |  |
| 7 | Akono | 33 | G | C |  |
| 8 | Akonolinga | 72 | G | B |  |
| 9 | Akum | 90 | G | B |  |
| 10 | Akwa Centre Dla | 84 | S | B |  |
| 11 | Akwa Nord Dla | 28 | S | C |  |
| 12 | Akwa, Laquintinie Dla | 40 | S | C |  |
| 13 | Aloum | 175 | G | A |  |
| 14 | Ashong | 65.11 | S | B |  |
| 15 | Assie | 70 | S | B |  |
| 16 | Asu Hill | 125 | G | A |  |
| 17 | Awae | 50 | S | C |  |
| 18 | Badionzou | 32 | S | C |  |
| 19 | Badzere | 72 | G | B |  |
| 20 | Bafang ancien | 12 | S | C |  |
| 21 | Bafang Nouveau | 50 | S | C |  |
| 22 | Bafia | 60 | S | B |  |
| 23 | Bafoussam Mux | 40 | S | C |  |
| 24 | Bafoussam radio | 123 | S | A |  |
| 25 | Baham nouveau | 50 | S | C |  |
| 26 | Bambouti | 96 | G | B |  |
| 27 | Bamenda ptt | 30 | S | C |  |
| 28 | Bamendjou | 30 | G | C |  |
| 29 | Banda | 96 | G | B |  |
| 30 | Bandal | 29 | S | C |  |
| 31 | BandaL | 29 | S | C |  |
| 32 | Bandjoun | 36 | S | C |  |
| 33 | Bangangte | 33 | S | C |  |
| 34 | Bangoua montagne | 50 | S | C |  |
| 35 | Banyo | 84 | G | B |  |
| 36 | Bardout | 90 | G | B |  |
| 37 | Bassa Logbaba Dla | 42 | S | C |  |
| 38 | Bastos ANOR Yde | 35 | S | C |  |
| 39 | Bastos, SIC Yde | 40 | S | C |  |
| 40 | Batibo | 38 | S | C |  |
| 41 | Batouri | 23 | G | C |  |
| 42 | Bembara | 108 | G | B |  |
| 43 | Bengbis | 45 | S | C |  |
| 44 | Bepanda | 40 | S | C |  |
| 45 | Bepanda térasse | 25 | S | C |  |
| 46 | Bepanda, Yong Yong | 40 | S | C |  |
| 47 | Bertoua Central | 45 | G | C |  |
| 48 | Betare Oya | 60 | S | B |  |
| 49 | Bidzar | 97 | G | B |  |
| 50 | BISSIANG | 50 | S | C |  |
| 51 | Biwong-Bulu | 70 | G | B |  |
| 52 | Biyem-Assi | 55 | S | B |  |
| 53 | Bokito | 60 | G | B |  |
| 54 | Bomono | 22 | G | C |  |
| 55 | Bonaberi | 34 | S | C |  |
| 56 | Bonaloka | 40 | S | C |  |
| 57 | Bonamoussadi Village | 40 | S | C |  |
| 58 | Bonanjo | 15 | S | C |  |
| 59 | Boulembe | 108 | G | B |  |
| 60 | Boumnyebel | 30 | G | C |  |
| 61 | Buea | 41 | S | C |  |
| 62 | University of Buea | 40 | S | C |  |
| 63 | CAMTEL HQ | 15+36 | S | B |  |
| 64 | Carriere Jean Vespa Yde | 40 | S | C |  |
| 65 | Chinde | 40 | S | C |  |
| 66 | Chuboh | 10 | S | C |  |
| 67 | Col Bana | 74 | G | B |  |
| 68 | Dang University of Ngaoundere | 40 | S | C |  |
| 69 | Diongo | 60 | G | B |  |
| 70 | Disso Patere | 160 | G | A |  |
| 71 | Djoum | 82 | G | B |  |
| 72 | Douala Omnisport DGSN | 40 | S | C |  |
| 73 | Douala PK21 | 40 | S | C |  |
| 74 | Dschang | 25 | S | C |  |
| 75 | Dzeng | 60 | S | B |  |
| 76 | Ebanga Ngoulou | 100 | G | B |  |
| 77 | Ebanga passif | 38 | S | C |  |
| 78 | Ebolowa comice | 40 | S | C |  |
| 79 | Ebolowa radio | 100 | G | B |  |
| 80 | Edea palmeraie | 162 | G | A |  |
| 81 | Efoulan | 82 | G | B |  |
| 82 | Ekie | 40 | S | C |  |
| 83 | Ekona | 56 | S | B |  |
| 84 | Elom | 51 | G | B |  |
| 85 | Emo | 140 | G | A |  |
| 86 | Eseka passif | 60 | G | B |  |
| 87 | Eseka PT | 15 | S | C |  |
| 88 | Etoug-Ebe, Collège Esp. | 40 | S | C |  |
| 89 | Evodoula | 60 | S | B |  |
| 90 | Figuil relais | 90 | G | B |  |
| 91 | Figuil ville | 50 | G | C |  |
| 92 | Fotokol | 90 | G | B |  |
| 93 | Foumban | 91 | G | B |  |
| 94 | Foumbot | 25 | S | C |  |
| 95 | Gaban-lara | 15 | S | C |  |
| 96 | Gangui | 72 | G | B |  |
| 97 | Garoua Central | 25 | S | C |  |
| 98 | Garoua radio | 50 | G | C |  |
| 99 | Garoua-Boulaï | 10 | S | C |  |
| 100 | Gouna | 96 | G | B |  |
| 101 | Goundaï | 15 | S | C |  |
| 102 | Guider | 31 | S | C |  |
| 103 | Guidiguis 1 | 25 | S | C |  |
| 104 | Guidiguis 2 | 70 | S | B |  |
| 105 | Jamot | 55 | S | B |  |
| 106 | Kaele | 36 | G | C |  |
| 107 | Katare | 120 | G | B |  |
| 108 | Kolofata | 18 | G | C |  |
| 109 | Konga | 108 | G | B |  |
| 110 | KOUM | 50 | S | C |  |
| 111 | Kousseri PT | 80 | S | B |  |
| 112 | Koweit City | 40 | S | C |  |
| 113 | Kribi PT | 45 | S | C |  |
| 114 | Kumba | 39 | S | C |  |
| 115 | Kumba Hill | 22 | S | C |  |
| 116 | Kumbo | 110 | G | B |  |
| 117 | Kurume | 118 | G | B |  |
| 118 | Kye-Ossi | 90 | G | B |  |
| 119 | Labado | 108 | G | B |  |
| 120 | Laf | 96 | G | B |  |
| 121 | Lara | 50 | S | C |  |
| 122 | Lembe Yezoum | 54 | G | B |  |
| 123 | Lere | 64 | G | B |  |
| 124 | Libong | 150 | G | A |  |
| 125 | Limbe | 33 | G | C |  |
| 126 | Limbe Kie | 40 | S | C |  |
| 127 | Lolodorf passif | 60 | G | B |  |
| 128 | Loum | 168 | G | A |  |
| 129 | Lycee Bilingue Bertoua | 40 | S | C |  |
| 130 | Maga | 90 | G | B |  |
| 131 | Malangue face HG | 40 | S | C |  |
| 132 | Mamfe | 41 | S | C |  |
| 133 | Mamfe | 24 | S | C |  |
| 134 | Mandassak | 130 | G | A |  |
| 135 | Manjo | 50 | S | C |  |
| 136 | Maroua Central | 42 | S | C |  |
| 137 | Maroua Pitoare | 40 | S | C |  |
| 138 | Maroua Radio | 90 | G | B |  |
| 139 | Matomb | 125 | G | A |  |
| 140 | Mayo Djinga | 70 | G | B |  |
| 141 | Mayo Oulo | 25 | S | C |  |
| 142 | Mayo Tolere | 155 | G | A |  |
| 143 | Mbalmayo | 70 | S | B |  |
| 144 | Mbandjock | 90 | G | B |  |
| 145 | Mbanga | 168 | G | A |  |
| 146 | Mbankolo | 25 | S | C |  |
| 147 | Mbankolo | 60 | G | B |  |
| 148 | Mbankolo | 100 | G | B |  |
| 149 | Mbe | 60 | S | B |  |
| 150 | Mbengwi | 60 | S | B |  |
| 151 | Mbengwi PTT | 50 | S | C |  |
| 152 | Mboma | 70 | S | B |  |
| 153 | Mbouda | 31 | G | C |  |
| 154 | Mbouda nouveau | 40 | S | C |  |
| 155 | Meba | 96 | G | B |  |
| 156 | Meiganga PT | 40 | S | C |  |
| 157 | Mekin | 85 | G | B |  |
| 158 | Melong | 50 | S | C |  |
| 159 | Memve’ele | 65 | G | B |  |
| 160 | Mendong, SIC | 40 | S | C |  |
| 161 | Mengangme | 91 | G | B |  |
| 162 | Mengbwa | 100 | G | B |  |
| 163 | Mengbwa | 118 | G | B |  |
| 164 | Mengong | 72 | G | B |  |
| 165 | Meyomessala | 100 | G | B |  |
| 166 | Meyomessala (SUDCAM) | 50 | S | C |  |
| 167 | Mfou | 30 | G | C |  |
| 168 | Mimboman Village | 40 | S | C |  |
| 169 | Mokolo | 55 | S | B |  |
| 170 | Monatele | 35 | S | C |  |
| 171 | Moneko’o | 60 | G | B |  |
| 172 | Muyuka | 31 | S | C |  |
| 173 | Mvoula | 70 | G | B |  |
| 174 | Nanga Eboko | 110 | G | B |  |
| 175 | Ndamukong | 40 | S | C |  |
| 176 | Ndem | 98 | G | B |  |
| 177 | Ndick | 60 | G | B |  |
| 178 | Ndikoum | 75 | G | B |  |
| 179 | Ndji | 96 | G | B |  |
| 180 | Ndogpassi | 40 | S | C |  |
| 181 | Ndogpassi 2 | 40 | S | C |  |
| 182 | Ndokayo | 96 | G | B |  |
| 183 | Ndoungue | 45 | S | C |  |
| 184 | New-Bell | 60 | G | B |  |
| 185 | Ngah | 102 | G | B |  |
| 186 | Ngaoundere Central | 40 | G | C |  |
| 187 | Ngoa Ekelle PTT | 40 | S | C |  |
| 188 | Ngoasse | 78 | G | B |  |
| 189 | Ngomezap | 60 | S | B |  |
| 190 | Ngong | 96 | G | B |  |
| 191 | NGOUDJEL(Fadil Ranch) | 70 | G | B |  |
| 192 | Nguti town | 37 | G | C |  |
| 193 | Njombe | 50 | G | C |  |
| 194 | Nkilzock | 72 | G | B |  |
| 195 | Nkoladjap | 60 | S | B |  |
| 196 | Nkolbisson | 40 | S | C |  |
| 197 | Nkoldobo | 40 | S | C |  |
| 198 | Nkolfong | 34 | G | C |  |
| 199 | Nkolndongo | 40 | S | C |  |
| 200 | Nkolyop | 62 | G | B |  |
| 201 | Nkometou | 40 | S | C |  |
| 202 | Nkondjock | 128 | G | A |  |
| 203 | Nkongmezap | 102 | G | B |  |
| 204 | Nkongsamba central | 24 | S | C |  |
| 205 | Nkongsamba radio | 115 | G | B |  |
| 206 | Nkoteng ADM | 18 | S | C |  |
| 207 | Nkoteng usine | 15 | S | C |  |
| 208 | Nkoumbent | 110 | G | B |  |
| 209 | Nsimalen | 30 | S | C |  |
| 210 | Ntoula | 18 | S | C |  |
| 211 | Ntui | 115 | G | B |  |
| 212 | Nyete Central office | 40 | G | C |  |
| 213 | Nyete V11 | 60 | S | B |  |
| 214 | Nyete V13 | 50 | S | C |  |
| 215 | Obala Ancien | 30 | S | C |  |
| 216 | Obala nouveau | 60 | S | B |  |
| 217 | Obili, IRIC | 40 | S | C |  |
| 218 | Odza, 11 Arrêt | 40 | S | C |  |
| 219 | Okola | 30 | S | C |  |
| 220 | Olamze | 30 | M | C |  |
| 221 | Ombessa | 70 | G | B |  |
| 222 | Oveng | 80 | G | B |  |
| 223 | Oyomabang Nkolsoo | 40 | S | C |  |
| 224 | Palmiers, Lycée | 40 | S | C |  |
| 225 | Pang | 155 | G | A |  |
| 226 | Pette | 90 | G | B |  |
| 227 | Pouma | 40 | S | C |  |
| 228 | Sa’a | 30 | G | C |  |
| 229 | Sangmelima PT | 69 | S | B |  |
| 230 | Signal Hill | 40 | S | C |  |
| 231 | Sikway | 30 | S | C |  |
| 232 | Simbock Village | 40 | S | C |  |
| 233 | Tatching | 50 | S | C |  |
| 234 | Tchatibali | 50 | S | C |  |
| 235 | Tchollire | 24 | S | C |  |
| 236 | Tibati PT | 24 | S | C |  |
| 237 | Tignere | 20 | S | C |  |
| 238 | Tiko | 38 | S | C |  |
| 239 | Tikondi | 67 | G | B |  |
| 240 | Tinto | 37 | S | C |  |
| 241 | Tombel | 60 | G | B |  |
| 242 | Waguri | 96 | G | B |  |
| 243 | Waza | 108 | G | B |  |
| 244 | Wum | 31 | S | C |  |
| 245 | Yabassi | 50 | S | C |  |
| 246 | Yagoua | 91 | G | B |  |
| 247 | Yassa Village | 40 | S | C |  |
| 248 | Yde Centre | 60 | S | B |  |
| 249 | Yett | 45 | G | C |  |
| 250 | Zamengoe | 53 | S | B |  |
| 251 | Zoetele | 72 | H | B |  |

# Text boxes

CAMTEL 2022 INTERCONNECTION, ACCESS, AND INFRASTRUCTURE-SHARING CATALOGUE

FOR THE MOBILE LICENCE

Current coverage

Planned coverage